## Slide 1
D1RPM v 3.0 PTV / VISUM
Tutorial:
Import CUBE model network into Visum

## Slide 2
Notes: Example: 2019 CUBE network. (from E:\D1\1-D1RPMv3.0 for deficiency plots-unzip\D1RPMv3.0 for deficiency plots\D1RPMv3.0\ ) NOTE: note the value for model key ZONESA, which is 6372 NOTE: in CUBE export links and nodes as shapefiles.

## Slide 3
Notes: PTV VISUM import for Cube Network

## Slide 4
Notes: Select nodes shapefile
NOTE: you will add 6372 to “maximum number of zones

## Slide 5
Notes: Import links shapefile

## Slide 6
Notes: NOTE: select A as from-node and B as to-node and select OK

## Slide 7
Notes: Progress window pop-up

## Slide 8
Notes: Imported model network, but it is not linked to any coordinate system so it will not overlay any maps in Visum.

## Slide 9
Notes: Select: Network>Network Settings>Co-ordinate system and “from file:” and select the highlighted projection.
Be sure to unselect the "Transform coordinates…” box.

## Slide 10
Notes: Now the model will overlay the default map as shown under the “world” drop-down list.

## Slide 11
Notes: At this point it would be a good idea to save the model version file, so you can return to this point in the future, if needed.

## Slide 12
Notes: You may post values ( BARS ) as usual in VISUM. Here the selected link from the CUBE assignment shows imported values as “IMPT_”+fieldname NOTE: total volume matches the original CUBE model network.